## Slide 1: Simple calculator
Exam Date: 2022/4/16

## Slide 2: Outline
Introduction
Instruction Set Architecture
Grammar
Operators and Variables
Example, Error Handling and Clock Cycles
Todo
Exam Reminder
More Details

## Slide 3: Outline
Introduction
Instruction Set Architecture
Grammar
Operators and Variables
Example, Error Handling and Clock Cycles
Todo
Exam Reminder
More Details

## Slide 4: Small computer
Let’s consider a CPU:
  Eight 32-bit registers r0-r7. 256-byte memory.
In this project, you need to implement a calculator.
  Input: a list of expressions, consisting of:
    Integers
    Operators (+, -, *, /, =, &, |, ^, ++, --)
    Three initial variables x, y, z (have initial values)
    Some new variables
  Output: A list of assembly code.
The instructions of the CPU and the clock cycle of each instruction are listed in the next page.

## Slide 5: Outline
Introduction
Instruction Set Architecture
Grammar
Operators and Variables
Example, Error Handling and Clock Cycles
Todo
Exam Reminder
More Details

## Slide 6: Instruction Set Architecture (I)
Opcode | Operand1 | Operand2 | Meaning | Cycles
MOV | Register1 | Register2 | Move data from register2 to register1 | 10
 | Register1 | Constant | Set the value of register1 constant | 10
 | Register1 | [Addr2] | Move the data (4 bytes) in memory addressed Addr2 to register1. Note that Addr2 must be a multiple of 4. | 200
 | [Addr1] | Register2 | Move the data (4 bytes) from register2 to the memory addressed Addr1. Note that Addr1 must be a multiple of 4. | 200

## Slide 7: Instruction Set Architecture (II)
Opcode | Operand1 | Operand2 | Meaning | Cycles
ADD | Register1 | Register2 | Add the value in register1 to register2 and store the result in register1 | 10
SUB | Register1 | Register2 | Subtract the value in register2 from the value in register1, and store the result in register1. | 10
MUL | Register1 | Register2 | Multiply the value in register1 to register2 and store the result in register1 | 30
DIV | Register1 | Register2 | Divide the value in register1 by the value in register2, and store the result in register1. Note it is the integer division. | 50
EXIT | Constant |  | Stop the program with a constant signal, whose value is specified as follows. 0: exit normally 1: the expression cannot be evaluated | 20

## Slide 8: Instruction Set Architecture (III)
Opcode | Operand1 | Operand2 | Meaning | Cycles
AND | Register1 | Register2 | Bitwise and the value in register1 to register2 and store the result in register1 | 10
OR | Register1 | Register2 | Bitwise or the value in register1 to register2 and store the result in register1 | 10
XOR | Register1 | Register2 | Bitwise exclusive or the value in register1 to register2 and store the result in register1 | 10

## Slide 9: Outline
Introduction
Instruction Set Architecture
Grammar
Operators and Variables
Example, Error Handling and Clock Cycles
Todo
Exam Reminder
More Details

## Slide 10: A complete grammar rules
You should modify the package code according to the grammar below
statement := ENDFILE | END | assign_expr END
assign_expr := ID ASSIGN assign_expr | or_expr
or_expr := xor_expr or_expr_tail
or_expr_tail := OR xor_expr or_expr_tail | NiL
xor_expr := and_expr xor_expr_tail
xor_expr_tail := XOR and_expr xor_expr_tail | NiL
and_expr := addsub_expr and_expr_tail
and_expr_tail := AND addsub_expr and_expr_tail | NiL
addsub_expr := muldiv_expr addsub_expr_tail
addsub_expr_tail := ADDSUB muldiv_expr addsub_expr_tail | NiL
muldiv_expr := unary_expr muldiv_expr_tail
muldiv_expr_tail := MULDIV unary_expr muldiv_expr_tail | NiL
unary_expr := ADDSUB unary_expr | factor
factor := INT | ID | INCDEC ID | LPAREN assign_expr RPAREN

## Slide 11: Tokens used in the grammar
INT: integer number
ID: variable
ASSIGN: =
LPAREN: (
RPAREN: )
END: ‘\n’
ENDFILE: EOF
ADDSUB: + or -
MULDIV: * or /
INCDEC: ++ or --
AND: &
OR: |
XOR: ^

## Slide 12: Binary Operators
Operator priority:
  [*, /] > [+, -] > & > ^ > |
&, |, ^ are the same as bitwise operators in C.
The left-hand side of an assignment (=) operator should be a variable.
Valid examples:
  x = 5
  x = y = 3
  x = (y = 1)
Invalid examples:
  5 = x
  x + y = 1
  (x + y) = 1

## Slide 13: Unary Operators
Two consecutive positive (+) or negative (-) signs should be regarded as a prefix increment/decrement operator. (e.g. ++x)
Only two consecutive (no spaces between) signs form an increment/decrement operator, e.g.
  ++x should be regarded as INC(++) x.
  + +x should be regarded as POSITIVE(+) POSITIVE(+) x.
The operand of an inc/dec operator should be a variable.
E.g. y=++5 or y=++(x+6) are both INVALID.

## Slide 14: Variables
Built-in variables x, y, z have initial values.
  Initially stored in memory [0], [4], [8] respectively.
When a NEW variable appears, there are two cases:
A variable first appears in the left-hand side of an assignment operator (=):
  Valid, and it can be used in the future
  E.g. c = x + 5, aa = bb = 3 * x are both valid.
A variable first appears in the right-hand side of an assignment operator (=):
  Invalid, and you should print EXIT 1
  E.g. x = cc * 5, if cc is a new variable, it is invalid.

## Slide 15: Variables
We guarantee that among all test cases, a new variable will NOT first appear in:
  Both side of an assignment operator (=)
    E.g. aa = aa + 1
  Prefix increment/decrement expression (++ or --)
    E.g. x = ++bb
Valid variable names may contain a-z, A-Z, numbers, and underscores(_) and may have arbitrary length.
Name of a variable should not start with a number
  Var_1 is valid, but 1_Var is invalid
  You should handle this error in your code
You should store the final values of x, y, z in registers r0, r1, r2 respectively before you print EXIT 0.

## Slide 16: Outline
Introduction
Instruction Set Architecture
Grammar
Operators and Variables
Example, Error Handling and Clock Cycles
Todo
Exam Reminder
More Details

## Slide 17: Example:
Input: x = z + 5
Output: (One of the possible outputs)
MOV r0, [0]
MOV r1, [4]
MOV r2, [8]
MOV r3, 5
ADD r3, r2
MOV r0, r3
EXIT 0
Read initial values from memory
Set a constant value 5 to r3
Add r3 (5) and r2 (z), and store the result to r3
Move the result from r3 to r0 (x)
Program ends

## Slide 18: Error handler
If the expression is invalid, such as
x = +3 % 5
y = (x+)
Your final output should be
EXIT 1
If the expression is invalid, no matter how many instructions you output, you should make sure your instructions contains an EXIT 1

## Slide 19: Error handler - Divide by zero
While doing division (/), if the right-hand side evaluates to zero, there are two cases:
No variable in the right-hand side:
  x = y / (1 + 2 - 3)
  This is an invalid expression.
At least one variable in the right-hand side:
  x = 0
  y = 5 / x
  This is a valid expression.

## Slide 20: Total clock cycles
Each instruction has an expected runtime:
  Specified by clock cycles (in the table)
The runtime of a program is:
  Sum of the clock cycles of all instructions.
Example: the following code has 90 clock cycles
MOV r0, 3 10 cc
MOV r1, 5 10 cc
MUL r0, r1 30 cc
MOV r1, 0 10 cc
MOV r2, 0 10 cc
EXIT 0 20 cc

## Slide 21: Outline
Introduction
Instruction Set Architecture
Grammar
Operators and Variables
Example, Error Handling and Clock Cycles
Todo
Exam Reminder
More Details

## Slide 22: Todo – lex.h / lex.c
Add some tokens to the TokenSet according to the complete grammar
  The grammar is in the previous slides
Modify the package code to accept new tokens
Make sure your code can accept variable names with multiple characters, numbers and underscores
  A variable starting with a number is invalid

## Slide 23: Todo – parser.h / parser.c
Add some parsing functions to handle the complete grammar
Do more error handling according to the grammar
Handle the undefined variable error
  The package code ignores this error now
Make sure you deal with the divide by zero error
  Detailed rules are in the previous slides

## Slide 24: Todo – codeGen.h / codeGen.c
Modify the evaluateTree() function to print assembly code
  The provided package only calculates the answer
Store the final values of x, y, z in registers r0, r1, r2 respectively before you print EXIT 0
Do some optimization to reduce total cycles of the generated assembly code to get extra credits
  You can use the provided assembly parser to calculate total cycles

## Slide 25: Outline
Introduction
Instruction Set Architecture
Grammar
Operators and Variables
Example, Error Handling and Clock Cycles
Todo
Exam Reminder
More Details

## Slide 26: Project parts
Assignment – Practice
  Trace the package code and complete the previously mentioned todo items.
  There will be a practice contest on OJ to verify your code during the whole project.
Exam – 100%
  An exam will be held on OJ to examine your comprehension of the assignment.
Extra Bonus (during exam):
  Optimize your code for the bonus points if you have time left and already get AC in the exam.

## Slide 27: Exam reminder (1)
There will be an online judge exam to test your comprehension of the assignment on 4/16 9-12.
The exam accounts for 100% of the total score of the whole project.
The exam will be a partial judge exam.

## Slide 28: Exam reminder (2)
Please make sure you complete the assignment before the exam day. The exam is highly related to the assignment.
Besides completing the todos, you should trace the whole package.

## Slide 29: Extra Bonus During Exam
If you have time left in the exam and already get AC, you can optimize your exam code for extra points.
Your code will be evaluated only if you get AC in the exam.
TAs will test the clock cycles of the assembly code generated by your latest AC exam code on OJ.
Students with fewer clock cycles get more extra bonus points.

## Slide 30: Outline
Introduction
Instruction Set Architecture
Grammar
Operators and Variables
Example, Error Handling and Clock Cycles
Todo
Demo Reminder
More Details

## Slide 31: Test case restriction
Only specified variables and signs are allowed.
  Allowed: + - * / ( ) & | ^ 0-9 a-z A-Z _
  Not allowed: @ # $ % … and more
  Symbols not allowed will not appear in test cases.
The result should follow the elementary arithmetic.
  x=2+3*4, x will be 14
  x=(2+3)*4, x will be 20
A test case may contain multiple expressions
Multiple expressions are separated by “\n”.

## Slide 32: Program output restrictions
You should print all the assembly code.
Don’t just print the result of x, y, z.
Ex: y = 1
z = 0
x = y + 5
One of the possible correct result will be:
  MOV r0, 0
  MOV r1, 1
  MOV r2, 0
  ADD r0, r1
  MOV r3, 5
  ADD r0, r3
  EXIT 0

## Slide 33: Others
You must deal with basic errors using EXIT 1.
  Extra or missing symbols (e.g. x = &|3 or x = y 3)
  Incorrect expression (e.g. 1 = 2 + 3 or ++y = 5)
You must deal with the uninitialized variable error
  Variables should appear in the left hand side of = first
  The provided package now ignores this error
Should be able to accept variables with arbitrary length
  E.g. var_1, tmpVal2 are both valid names
Should be able to calculate numbers > 10.
  E.g. x = 11
Should be able to calculate long expressions.
  E.g. x = 4-x/z*33+4+20*31+10